## Slide 1
Reference, Retention and Reserve Samples

## Slide 2: Definition (1)
REFERENCE SAMPLE (EU):
  A sample of a batch of starting material, packaging material or finished product stored for the purpose of being analyzed should the need arise during the shelf life of the batch concerned
  Critical intermediate or intermediate when sufficient stability
  Sufficient size to permit at least two occasions full analytical

## Slide 3: Definition (2)
RETENTION SAMPLE (EU):
  A sample of a fully packaged unit from a batch of finished product stored for identification purposes
  In many instances, reference and retention samples of finished products are presented identically. In such circumstances, reference and retention samples may be regarded as interchangeable.

## Slide 4: Definition (3)
RESERVE SAMPLE (US):
  A sample representative of each lot in each shipment of each active ingredient or a sample representative of each lot of drug product
  At least two times the quantity necessary for all tests required to determine whether the API or drug product meets its established specifications
  Drug products must be stored in the same container-closure in which it is marketed.

## Slide 5: Scope
APPLICABLE TO:
All pharmaceutical manufacturing and distribution sites
All affiliates
All GMP/GDP Subcontractors

## Slide 6: Reference Documents (1)
EU: EC - Volume 4 – GMP
  Chapter 1: Quality Management – Quality Control 1.4 (VIII)
  Chapter 6: Quality Control - Sampling 6.12 and 6.14
  Annex 19: Reference and retention Samples

## Slide 7: Reference Documents (2)
US: FDA
  21 CFR 211.170 Reserve Samples
  21 CFR 211.180 (e) Records and Reports, General Requirements

## Slide 8: Reference Documents (3)
ICH
  Guideline Q 7 A GMP for Active Pharmaceutical Ingredients paragraph 11.7 Reserve/Retention Samples

## Slide 9: General Requirements (1)
Requirements for retention samples (EU) apply to reserve samples (US)
Reference/Reserve Samples should be of sufficient size to permit, on at least two occasions, a full analytical control (including sterility and pyrogens). Exception must be approved by Site Quality Management and agreed with relevant competent authority.

## Slide 10: General Requirements (2)
When batch is packaged in two or more packaging operations (e.g. for different markets),one retention sample taken from each individual packaging operation
The exception to this will be when a small amount of a batch is packaged for different markets or in case of very expensive medicinal product then only one retention sample can be taken.

## Slide 11: General Requirements (3)
Reference samples of each batch of the following must be kept at the site at which they were used:
  starting material
  intermediate product
  primary and printed packaging material*
*The printed materials as part of the reference
and/or retention sample of the finished product
can also be accepted as reference materials.

## Slide 12: General Requirements (4)
Must be Stored in a secure area and under conditions consistent with specified storage conditions for material or finished product
Storage conditions must be recorded. In case of deviation from specified conditions, document, investigate and assess impact for each retention sample
Access to these samples limited to authorized people
Quality must authorise and documented any withdrawal of any reference/retention samples.

## Slide 13: API Sample Retention Period
API samples should be retained for a time period covering API shelf-life plus 6 years (covers potential maximum 5 years shelf-life of finished product)
Same retention principle generally applies for API intermediates as finished product however the intermediate may have a different SL than the finished product therefore the above point will apply.

## Slide 14: API Storage Requirements
API samples should be stored in same packaging system as marketed packaging system
API intermediate samples should also be stored in same packaging system as marketed packaging system.

## Slide 15: Storage Requirements for APIs, Excipients and Packaging Materials (1)
Samples of APIs and excipients must be retained (solvents, water, gases used in manufacturing process are excluded)
Sample containers must assure APIs and excipients are protected throughout the retention period
Retention period:
  Excipients and API: one year after the shelf-life of drug product and at least two years after release of the finished product if local regulations allow (EU)
  Time period may be shortened if material stability period is shorter.

## Slide 16: Storage Requirements for APIs, Excipients and Packaging Materials (2)
Retention period (cont.)
  Packaging material must be retained for the duration of shelf-life of finished product concerned (EU regulation).

## Slide 17: Storage Requirements for Finished Product
Samples must be retained in marketed primary and secondary packaging
Retention period:
  Minimum one year after expiry of finished product
Location:
  Reference and Retention samples stored at the site that releases the finished product and/or according specific local requirements (Canada, EU).

## Slide 18: Storage Requirements for Controlled Drugs
Stored separate from other samples and protection against forced entry
Only authorised personnel must have access to controlled drug area
Monitoring and reconciliation logbook is mandatory, there must be a defined retention period for logbook after the date of last product sampling.

## Slide 19: Reserve Samples - Finished Product
Visual examination of representative lots of retention (reserve) samples to be performed if required by local regulation (products marketed within the US or for the US market)
Examination of finished products reserve samples required during complaint investigation and as part of Annual Product Review (products marketed within the US or for the US market).

## Slide 20
Thank You
Any Questions